## Slide 1
Computer Networking: A Top-Down Approach 8th edition Jim Kurose, Keith Ross Pearson, 2020
Chapter 6 The Link Layer
and LANs
A note on the use of these PowerPoint slides:
We’re making these slides freely available to all (faculty, students, readers). They’re in PowerPoint form so you see the animations; and can add, modify, and delete slides (including this one) and slide content to suit your needs. They obviously represent a lot of work on our part. In return for use, we only ask the following:
If you use these slides (e.g., in a class) that you mention their source (after all, we’d like people to use our book!)
If you post any slides on a www site, that you note that they are adapted from (or perhaps identical to) our slides, and note our copyright of this material.
For a revision history, see the slide note for this page.
Thanks and enjoy! JFK/KWR
All material copyright 1996-2020
J.F Kurose and K.W. Ross, All Rights Reserved
Notes: Version History
8.0 (May 2020)
All slides reformatted for 16:9 aspect ratio
All slides updated to 8th edition material
Use of Calibri font, rather that Gill Sans MT
Add LOTS more animation throughout
lighter header font
Updated datacenter slides, day-in-the-life

## Slide 2: Link layer and LANs: our goals
understand principles behind link layer services:
  error detection, correction
  sharing a broadcast channel: multiple access
  link layer addressing
  local area networks: Ethernet, VLANs
datacenter networks
instantiation, implementation of various link layer technologies

## Slide 3: Link layer, LANs: roadmap
a day in the life of a web request
introduction
error detection, correction
multiple access protocols
LANs
  addressing, ARP
  Ethernet
  switches
  VLANs
link virtualization: MPLS
data center networking

## Slide 4: Link layer: introduction
terminology:
hosts and routers: nodes
communication channels that connect adjacent nodes along communication path: links
  wired
  wireless
  LANs (Local Area Networks)
layer-2 packet: frame, encapsulates datagram
mobile network
enterprise
network
national or global ISP
datacenter
network
link layer has responsibility of
transferring datagram from one node
to physically adjacent node over a link

## Slide 5: Link layer: context
datagram transferred by different link protocols over different links:
  e.g., WiFi on first link, Ethernet on next link
each link protocol provides different services
  e.g., may or may not provide reliable data transfer over link
transportation analogy:
trip from Princeton to Lausanne
  limo: Princeton to JFK
  plane: JFK to Geneva
  train: Geneva to Lausanne
tourist = datagram
transport segment = communication link
transportation mode = link-layer protocol
travel agent = routing algorithm

## Slide 6: Link layer: services
framing, link access:
  encapsulate datagram into frame, adding header, trailer
  channel access if shared medium
  “MAC” addresses in frame headers identify source, destination (different from IP address!)
reliable delivery between adjacent nodes
  we already know how to do this!
  seldom used on low bit-error links
  wireless links: high error rates
    Q: why both link-level and end-end reliability?
…
…

## Slide 7: Link layer: services (more)
flow control:
  pacing between adjacent sending and receiving nodes
error detection:
  errors caused by signal attenuation, noise.
  receiver detects errors, signals retransmission, or drops frame
error correction:
  receiver identifies and corrects bit error(s) without retransmission
half-duplex and full-duplex:
  with half duplex, nodes at both ends of link can transmit, but not at same time
…
…

## Slide 8: Where is the link layer implemented?
in each-and-every host
link layer implemented in network interface card (NIC) or on a chip
  Ethernet, WiFi card or chip
  implements link, physical layer
attaches into host’s system buses
combination of hardware, software, firmware
controller
physical
cpu
memory
host bus
(e.g., PCI)
network interface
application
transport
network
link
link
physical

## Slide 9: Interfaces communicating
controller
physical
memory
CPU
controller
physical
cpu
memory
application
transport
network
link
link
physical
application
transport
network
link
link
physical
sending side:
encapsulates datagram in frame
adds error checking bits, reliable data transfer, flow control, etc.
receiving side:
looks for errors, reliable data transfer, flow control, etc.
extracts datagram, passes to upper layer at receiving side
linkh
linkh
datagram
datagram
datagram

## Slide 10: Link layer, LANs: roadmap
a day in the life of a web request
introduction
error detection, correction
multiple access protocols
LANs
  addressing, ARP
  Ethernet
  switches
  VLANs
link virtualization: MPLS
data center networking

## Slide 11: Error detection
EDC: error detection and correction bits (e.g., redundancy)
D: data protected by error checking, may include header fields
Error detection not 100% reliable!
  protocol may miss some errors, but rarely
  larger EDC field yields better detection and correction
datagram
D
EDC
d data bits
bit-error prone link
D’
EDC’
all
bits in D’
OK
?
N
detected
error
otherwise
datagram

## Slide 12: Parity checking
single bit parity:
detect single bit errors
0111000110101011
1
parity
bit
d data bits
two-dimensional bit parity:
detect and correct single bit errors
d1,1
d2,1
di,1
. . .
d1,j+1
d2,j+1
di,j+1
. . .
. . .
d1,j
d2,j
di,j
. . .
di+1,1
di+1,j+1
di+1,j
. . .
. . .
. . .
. . .
row parity
column
parity
0 1 1 1 0 1
1 0 1 0 1 1
1 1 1 1 0 0
1 0 1 0 1 0
no errors:
0 1 1 1 0 1
1 0 1 0 1 1
1 0 1 1 0 0
1 0 1 0 1 0
parity
error
parity
error
detected
and
correctable
single-bit
error:
Even parity: set parity bit so there is an even number of 1’s
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/

## Slide 13: Internet checksum (review)
sender:
treat contents of UDP segment (including UDP header fields and IP addresses) as sequence of 16-bit integers
checksum: addition (one’s complement sum) of segment content
checksum value put into UDP checksum field
receiver:
compute checksum of received segment
check if computed checksum equals checksum field value:
  not equal - error detected
  equal - no error detected. But maybe errors nonetheless? More later ….
Goal: detect errors (i.e., flipped bits) in transmitted segment

## Slide 14: Cyclic Redundancy Check (CRC)
more powerful error-detection coding
D: data bits (given, think of these as a binary number)
G: bit pattern (generator), of r+1 bits (given)
goal: choose r CRC bits, R, such that <D,R> exactly divisible by G (mod 2)
  receiver knows G, divides <D,R> by G. If non-zero remainder: error detected!
  can detect all burst errors less than r+1 bits
  widely used in practice (Ethernet, 802.11 WiFi)
r CRC bits
d data bits
D
R
<D,R> = D 2r XOR R
*
bit pattern
formula for bit pattern

## Slide 15: Cyclic Redundancy Check (CRC): example
We want:
  D.2r XOR R = nG
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/
D.2r
G
R = remainder [ ]
or equivalently:
  D.2r = nG XOR R
or equivalently:
if we divide D.2r by G, want remainder R to satisfy:
1 0 0 1
1 0 1 0
1 0 1
0 0 0
1 0 0 1
1 0 0 1
1 0 0 1
0 0 0
1 1 0
1 1 0 0
1 0 1 0
0 1 1
0 1 1
D
R
1 0 0 1
G
0 0 0
1 0 1 1 1 0
2r
*
1
0
1

## Slide 16: Step 1: CRC Encoding Method
Let us view each block of data as a polynomial with binary coefficients:
  1 0 1 1 0 1 is viewed as x 5 + x 3 + x 2 + 1
Define:
D(x): Data block is a polynomial (= Message, Frame)
P(x): Generator Polynomial, which is known to both sender and receiver (degree of P(x) is n)

## Slide 17: Step 2: Arithmetic
Modulo-2 Arithmetic:
  addition/subtraction without carries
  Same as the exclusive-OR (XOR)
Examples of polynomials based on Modulo-2 operations:
  1. (x+1)(x+1) = x2+1
  2. (x2+1)(x3+x+1) = x5+x2+x+1

## Slide 18: Step 2: CRC Encoding Method
Append n zeros to Data, i.e., multiply D(x) by xn
Divide D(x)xn by P(x) and obtain:
D(x) xn = Q(x) P(x) + R(x)
Set T(x) = D(x) xn + R(x), T(x) is the encoded message
  T(x) = [Q(x)P(x) + R(x)] + R(x) = Q(x)P(x)
  T(x) divisible by P(x)
Received message Tr contains error? Or Tr(x) == T(x) ?
If Tr (x) does not contain an error, then it can be divided by P(x) <=> if Tr (x) cannot be divided by P(x), it must contain error!
How about: if Tr (x) can be divided by P(x), is it always error-free?

## Slide 19: Step 3: Encoding
D(x) = x9 + x8 + x6 + x4 + x3 + x + 1
    Generator polynomial is P(x) = x4 + x + 1
    Degree of P(x) is 4
(I) D(x) x4 = x13 + x12 + x10 + x8 + x7 + x5 + x4
(II) D(x) x4 = Q(x) P(x) + R(x) =(x9 + x8 + x3 + x) P(x) + x3 + x2 + x
(III) T(x) = D(x) x4 + R(x)
= x13 + x12 + x10 + x8 + x7 + x5 + X4 + x3 + x2 + x
Transmitted Bit Sequence: 1 1 0 1 0 1 1 0 1 1 1 1 1 0

## Slide 20: Example of Generating a CRC

## Slide 21: Step 4: Error Detection with CRC
Errors can be expressed as Error Polynomials
For example,
    Sent Message: 1 0 1 1 1 0 1
    Received Message: 1 1 1 1 0 0 1
    ______________________________
    Error: 0 1 0 0 1 0 0
In the example, the Error Polynomial E(x) is given by: E(x) = x 5 + x 2
Received Polynomial
  Tr (x) = T(x) + E(x)

## Slide 22: Step 5: Error Detection Capability of CRC
Note:
Errors will NOT be detected by CRC,
if E(x) contains P(x) as a factor: E(x) = B(x) P(x)
    Tr (x) = T(x) + E(x) = [Q(x) + B(x)] P(x)
    If Tr (x) is divisible by P(x), receiver mistakenly assumes no error!
Observe the following trade-off:
  Strong CRC: chances that error pattern is divisible by P(x) is small, therefore increasing the error detection capability.
  The higher degree n of P(x), the stronger CRC
  Large values of n introduce high overhead but improve the error detection capability.

## Slide 23: Step 5: Error Detection Capability of CRC
All single-bit errors are detected, if P(x) has a factor with at least 2 terms
All double-bit errors are detected, if P(x) has a factor with at least 3 terms
If P(x) contains (x+1) as a factor, then all errors with “odd” number of bits are detected.
  CRC detects 50% of all errors
An n-bit CRC checksum detects all burst errors of length  n bits. (A burst error of length n is a string of n bits in which the first and last are in error, and the intermediate n – 2 bits may or may not be in error.)

## Slide 24: CRC Implementations
CRC can be efficiently implemented in hardware by a set of XOR gates and a shift register
The following generator polynomials are widely used:
CRC-12: P(x) = x 12 + x 11 + x 3 + x 2 + x + 1
CRC-16: P(x) = x 16 + x 15 + x 2 + 1
CRC-CCITT: P(x) = x 16 + x 12 + x 5 + 1
CRC-32: P(x) = x 32 + x 26 + x 23 + x 22 + x 16 + x 12 + x 11 + x 10 + x 8 + x7 + x 5 + x 4 + x 2 + x + 1

## Slide 25: CRC Implementations
P(x) = x 3 + x + 1, Message: M = 11001011
Scheme 1: append 3 0-bits to the message and feeds it from the right. The CRC register will have the checksum after L+3 clocks, where L is the message length.
Scheme 2: feed the message at the left end. No need to append the 3 0-bits. Hence, faster. The CRC result is obtained after L clocks.

## Slide 26: CRC-32 Implementation for Ethernet
P(x) = x 32 + x 26 + x 23 + x 22 + x 16 + x 12 + x 11 + x 10 + x 8 + x7 + x 5 + x 4 + x 2 + x + 1

## Slide 27: Link layer, LANs: roadmap
a day in the life of a web request
introduction
error detection, correction
multiple access protocols
LANs
  addressing, ARP
  Ethernet
  switches
  VLANs
link virtualization: MPLS
data center networking

## Slide 28: Multiple access links, protocols
two types of “links”:
point-to-point
  point-to-point link between Ethernet switch, host
  PPP for dial-up access
broadcast (shared wire or medium)
  old-fashioned Ethernet
  upstream HFC in cable-based access network
  802.11 wireless LAN, 4G/4G. satellite
shared wire (e.g.,
cabled Ethernet)
shared radio: WiFi
shared radio: satellite
humans at a cocktail party
(shared air, acoustical)
shared radio: 4G/5G

## Slide 29: Multiple access protocols
single shared broadcast channel
two or more simultaneous transmissions by nodes: interference
  collision if node receives two or more signals at the same time
distributed algorithm that determines how nodes share channel, i.e., determine when node can transmit
communication about channel sharing must use channel itself!
  no out-of-band channel for coordination
multiple access protocol

## Slide 30: An ideal multiple access protocol
given: multiple access channel (MAC) of rate R bps
desiderata (desired objectives):
  1. when one node wants to transmit, it can send at rate R.
  2. when M nodes want to transmit, each can send at average rate R/M
  3. fully decentralized:
    no special node to coordinate transmissions
    no synchronization of clocks, slots
  4. simple

## Slide 31: MAC protocols: taxonomy
three broad classes:
channel partitioning
  divide channel into smaller “pieces” (time slots, frequency, code)
  allocate piece to node for exclusive use
random access
  channel not divided, allow collisions
  “recover” from collisions
“taking turns”
  nodes take turns, but nodes with more to send can take longer turns

## Slide 32: Channel partitioning MAC protocols: TDMA
TDMA: time division multiple access
access to channel in “rounds”
each station gets fixed length slot (length = packet transmission time) in each round
unused slots go idle
example: 6-station LAN, 1,3,4 have packets to send, slots 2,5,6 idle
1
3
4
1
3
4
6-slot
frame
6-slot
frame

## Slide 33: Channel partitioning MAC protocols: FDMA
FDMA: frequency division multiple access
channel spectrum divided into frequency bands
each station assigned fixed frequency band
unused transmission time in frequency bands go idle
example: 6-station LAN, 1,3,4 have packet to send, frequency bands 2,5,6 idle
frequency bands
time
FDM cable

## Slide 34: Random access protocols
when node has packet to send
  transmit at full channel data rate R.
  no a priori coordination among nodes
two or more transmitting nodes: “collision”
random access MAC protocol specifies:
  how to detect collisions
  how to recover from collisions (e.g., via delayed retransmissions)
examples of random access MAC protocols:
  ALOHA, slotted ALOHA
  CSMA, CSMA/CD, CSMA/CA

## Slide 35: Slotted ALOHA
assumptions:
all frames same size
time divided into equal size slots (time to transmit 1 frame)
nodes start to transmit only slot beginning
nodes are synchronized
if 2 or more nodes transmit in slot, all nodes detect collision
operation:
when node obtains fresh frame, transmits in next slot
  if no collision: node can send new frame in next slot
  if collision: node retransmits frame in each subsequent slot with probability p until success
randomization – why?

## Slide 36: Slotted ALOHA
Pros:
single active node can continuously transmit at full rate of channel
highly decentralized: only slots in nodes need to be in sync
simple
Cons:
collisions, wasting slots
idle slots (why?)
nodes may be able to detect collision in less than time to transmit packet (a slot)
clock synchronization
1
1
1
1
2
3
2
2
3
3
node 1
node 2
node 3
C
C
C
S
S
S
E
E
E
C: collision
S: success
E: empty

## Slide 37: Slotted ALOHA: efficiency
efficiency: long-run fraction of successful slots (many nodes, all with many frames to send)
suppose: N nodes with many frames to send, each transmits in slot with probability p
  prob that given node has success in a slot = p(1-p)N-1
  prob that any node has a success = Np(1-p)N-1
  max efficiency: find p* that maximizes Np(1-p)N-1
  for many nodes, take limit of Np*(1-p*)N-1 as N goes to infinity, gives:
max efficiency = 1/e = .37
at best: channel used for useful transmissions 37% of time!

## Slide 38: Pure ALOHA
unslotted Aloha: simpler, no synchronization
  when frame first arrives, transmit immediately
collision probability increases with no synchronization:
  i’s frame sent at t0 collides with other frames sent in [t0-1,t0+1]
t0 + 1
t0 - 1
t0
will overlap
with end of
i’s frame
will overlap
with start of
i’s frame
pure Aloha efficiency: 18% !

## Slide 39: CSMA (carrier sense multiple access)
simple CSMA: listen before transmit:
  if channel sensed idle: transmit entire frame
  if channel sensed busy: defer transmission
human analogy: don’t interrupt others!
CSMA/CD: CSMA with collision detection
  collisions detected within short time
  colliding transmissions aborted, reducing channel wastage
  collision detection easy in wired, difficult with wireless
human analogy: the polite conversationalist

## Slide 40: CSMA: collisions
collisions can still occur with carrier sensing:
  propagation delay means two nodes may not hear each other’s just-started transmission
collision: entire packet transmission time wasted
  distance & propagation delay play role in determining collision probability
spatial layout of nodes

## Slide 41: CSMA/CD:
CSMA/CS reduces the amount of time wasted in collisions
  transmission aborted on collision detection
spatial layout of nodes

## Slide 42: Ethernet CSMA/CD algorithm
NIC receives datagram from network layer, creates frame
If NIC senses channel:
  if idle: start frame transmission.
  if busy: wait until channel idle, then transmit
If NIC transmits entire frame without collision, NIC is done with frame !
If NIC detects another transmission while sending: abort, send jam signal
After aborting, NIC enters binary (exponential) backoff:
  after m-th collision, NIC chooses K at random from {0,1,2, …, 2m-1}. NIC waits K·512 bit times, returns to Step 2
  more collisions: longer backoff interval
  After 10 or more collisions, K is chosen with equal probability from {0,1,2,..., 1023}

## Slide 43: CSMA/CD efficiency
Tprop = max prop delay between 2 nodes in LAN
ttrans = time to transmit max-size frame
efficiency goes to 1
  as tprop goes to 0
  as ttrans goes to infinity
better performance than ALOHA, and simple, cheap, decentralized!

## Slide 44: “Taking turns” MAC protocols
channel partitioning MAC protocols:
  share channel efficiently and fairly at high load
  inefficient at low load: delay in channel access, 1/N bandwidth allocated even if only 1 active node!
random access MAC protocols
  efficient at low load: single node can fully utilize channel
  high load: collision overhead
“taking turns” protocols
  look for best of both worlds!

## Slide 45: “Taking turns” MAC protocols
polling:
master node “invites” other nodes to transmit in turn
typically used with “dumb” devices
concerns:
  polling overhead in time and bandwidth
  latency
  single point of failure (master)
master
slaves
poll
data
data

## Slide 46: “Taking turns” MAC protocols
token passing:
control token passed from one node to next sequentially.
token message
concerns:
  token overhead
  latency
  single point of failure (token missing)
T
data
(nothing
to send)
T

## Slide 47: Cable access network: FDM, TDM and random access!
cable headend
CMTS
ISP
cable modem
termination system
cable
modem
splitter
…
…
Internet frames, TV channels, control transmitted
downstream at different frequencies
multiple downstream (broadcast) FDM channels: up to 1.6 Gbps/channel
  single CMTS transmits into channels
multiple upstream channels (up to 1 Gbps/channel)
  multiple access: all users contend (random access) for certain upstream channel time slots; others assigned TDM

## Slide 48: Cable access network:
DOCSIS: data over cable service interface specification
FDM over upstream, downstream frequency channels
TDM upstream: some slots assigned, some have contention
  downstream MAP frame: assigns upstream slots for each modem
  request for upstream slots (and data) transmitted random access (binary backoff) in selected slots
  A cable modem infers that its mini-slot-request frame experienced a collision if it does not receive a response to the requested allocation in the next downstream control message
Residences with cable modems
Downstream channel i
Upstream channel j
MAP frame for
Interval [t1, t2]
t1
t2
Assigned minislots containing cable modem
upstream data frames
Minislots containing
minislots request frames
cable headend
CMTS

## Slide 49: Summary of MAC protocols
channel partitioning, by time, frequency or code
  Time Division, Frequency Division
random access (dynamic),
  ALOHA, S-ALOHA, CSMA, CSMA/CD
  carrier sensing: easy in some technologies (wire), hard in others (wireless)
  CSMA/CD used in Ethernet
  CSMA/CA used in 802.11
taking turns
  polling from central site, token passing
  Bluetooth, FDDI, token ring
A cable access network serves as a terrific example of MAC protocols in action—FDM, TDM, random access, and centrally allocated time slots all within one network!

## Slide 50: Link layer, LANs: roadmap
a day in the life of a web request
introduction
error detection, correction
multiple access protocols
LANs
  addressing, ARP
  Ethernet
  switches
  VLANs
link virtualization: MPLS
data center networking

## Slide 51: MAC addresses
32-bit IP address:
  network-layer address for interface
  used for layer 3 (network layer) forwarding
  e.g.: 128.119.40.136
MAC (or LAN or physical or Ethernet) address:
  function: used “locally” to get frame from one interface to another physically-connected interface (same subnet, in IP-addressing sense)
  48-bit MAC address (for most LANs) burned in NIC ROM, also sometimes software settable
hexadecimal (base 16) notation
(each “numeral” represents 4 bits)
  e.g.: 1A-2F-BB-76-09-AD

## Slide 52: MAC addresses
each interface on LAN
has unique 48-bit MAC address
has a locally unique 32-bit IP address
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
(wired or wireless)
137.196.7/24
137.196.7.78
137.196.7.14
137.196.7.88
137.196.7.23

## Slide 53: MAC addresses
MAC address allocation administered by IEEE
manufacturer buys portion of MAC address space (to assure uniqueness)
analogy:
  MAC address: like Social Security Number
  IP address: like postal address
MAC flat address: portability
  can move interface from one LAN to another
  recall IP address not portable: depends on IP subnet to which node is attached

## Slide 54: ARP: address resolution protocol
ARP table: each IP node (host, router) on LAN has table
Question: how to determine interface’s MAC address, knowing its IP address?
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
137.196.7.78
137.196.7.14
137.196.7.88
137.196.7.23
ARP
ARP
ARP
ARP
  IP/MAC address mappings for some LAN nodes:
< IP address; MAC address; TTL>
  TTL (Time To Live): time after which address mapping will be forgotten (typically 20 min)

## Slide 55: ARP protocol in action
58-23-D7-FA-20-B0
137.196.7.14
B
C
D
TTL
71-65-F7-2B-08-53
137.196.7.23
A
ARP table in A
IP addr
MAC addr
TTL
example: A wants to send datagram to B
  B’s MAC address not in A’s ARP table, so A uses ARP to find B’s MAC address
A broadcasts ARP query, containing B's IP addr
  destination MAC address = FF-FF-FF-FF-FF-FF
  all nodes on LAN receive ARP query
1
Source MAC: 71-65-F7-2B-08-53
Source IP: 137.196.7.23
Target IP address: 137.196.7.14
…
1
Ethernet frame (sent to FF-FF-FF-FF-FF-FF)

## Slide 56: ARP protocol in action
58-23-D7-FA-20-B0
137.196.7.14
B
C
D
TTL
71-65-F7-2B-08-53
137.196.7.23
A
ARP table in A
IP addr
MAC addr
TTL
example: A wants to send datagram to B
  B’s MAC address not in A’s ARP table, so A uses ARP to find B’s MAC address
B replies to A with ARP response, giving its MAC address
2
Target IP address: 137.196.7.14
Target MAC address:
58-23-D7-FA-20-B0
…
2
ARP message into Ethernet frame (sent to 71-65-F7-2B-08-53)

## Slide 57: ARP protocol in action
58-23-D7-FA-20-B0
137.196.7.14
B
C
D
TTL
71-65-F7-2B-08-53
137.196.7.23
A
ARP table in A
IP addr
MAC addr
TTL
example: A wants to send datagram to B
  B’s MAC address not in A’s ARP table, so A uses ARP to find B’s MAC address
A receives B’s reply, adds B entry into its local ARP table
3
137.196.
7.14
58-23-D7-FA-20-B0
500

## Slide 58: Routing to another subnet: addressing
walkthrough: sending a datagram from A to B via R
  focus on addressing – at IP (datagram) and MAC layer (frame) levels
R
A
B
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
  assume that:
    A knows B’s IP address
    A knows IP address of first hop router, R (how?)*
    A knows R’s MAC address (how?)
* A DHCP server provides an IP address for the host, as well as the IP address of the DNS server, the IP address for the default gateway router, and the subnet network mask.

## Slide 59: Routing to another subnet: addressing
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP
Eth
Phy
IP src: 111.111.111.111
IP dest: 222.222.222.222
A creates IP datagram with IP source A, destination B
A creates link-layer frame containing A-to-B IP datagram
  R's MAC address is frame’s destination
MAC src: 74-29-9C-E8-FF-55
MAC dest: E6-E9-00-17-BB-4B

## Slide 60: Routing to another subnet: addressing
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP
Eth
Phy
frame sent from A to R
IP
Eth
Phy
frame received at R, datagram removed, passed up to IP
MAC src: 74-29-9C-E8-FF-55
MAC dest: E6-E9-00-17-BB-4B
IP src: 111.111.111.111
IP dest: 222.222.222.222
IP src: 111.111.111.111
IP dest: 222.222.222.222

## Slide 61: Routing to another subnet: addressing
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP src: 111.111.111.111
IP dest: 222.222.222.222
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
R determines outgoing interface, passes datagram with IP source A, destination B to link layer
R creates link-layer frame containing A-to-B IP datagram. Frame destination address: B's MAC address
IP
Eth
Phy

## Slide 62: Routing to another subnet: addressing
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP
Eth
Phy
IP
Eth
Phy
IP src: 111.111.111.111
IP dest: 222.222.222.222
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
transmits link-layer frame
R determines outgoing interface, passes datagram with IP source A, destination B to link layer
R creates link-layer frame containing A-to-B IP datagram. Frame destination address: B's MAC address

## Slide 63: Routing to another subnet: addressing
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP
Eth
Phy
IP
Eth
Phy
B receives frame, extracts IP datagram destination B
B passes datagram up protocol stack to IP
IP src: 111.111.111.111
IP dest: 222.222.222.222

## Slide 64: Link layer, LANs: roadmap
a day in the life of a web request
introduction
error detection, correction
multiple access protocols
LANs
  addressing, ARP
  Ethernet
  switches
  VLANs
link virtualization: MPLS
data center networking

## Slide 65: Ethernet
“dominant” wired LAN technology:
first widely used LAN technology
simpler, cheap
kept up with speed race: 10 Mbps – 400 Gbps
single chip, multiple speeds (e.g., Broadcom BCM5761)
Metcalfe’s Ethernet sketch
https://www.uspto.gov/learning-and-resources/journeys-innovation/audio-stories/defying-doubters

## Slide 66: Ethernet: physical topology
bus: popular through mid 90s
  all nodes in same collision domain (can collide with each other)
bus: coaxial cable
switched
switched: prevails today
  active link-layer 2 switch in center
  each “spoke” runs a (separate) Ethernet protocol (nodes do not collide with each other)

## Slide 67: Ethernet frame structure
sending interface encapsulates IP datagram (or other network layer protocol packet) in Ethernet frame
dest.
address
source
address
data (payload)
CRC
preamble
type
preamble:
used to synchronize receiver, sender clock rates
7 bytes of 10101010 followed by one byte of 10101011
Payload size: 46-1500 bytes. Minimum payload size (46 bytes) is dictated by the 512-bit slot time used for collision detection in the Ethernet LAN architecture
Interpacket gap: After a packet has been sent, transmitters are required to transmit a minimum of 12 bytes of idle line state before transmitting the next packet.
Inter. gap

## Slide 68: Ethernet frame structure (more)
dest.
address
source
address
data (payload)
CRC
preamble
type
addresses: 6 byte source, destination MAC addresses
  if adapter receives frame with matching destination address, or with broadcast address (e.g., ARP packet), it passes data in frame to network layer protocol
  otherwise, adapter discards frame
type: indicates higher layer protocol
  mostly IP but others possible, e.g., Novell IPX, AppleTalk
  used to demultiplex up at receiver
CRC: cyclic redundancy check at receiver
  error detected: frame is dropped

## Slide 69: Ethernet: unreliable, connectionless
connectionless: no handshaking between sending and receiving NICs
unreliable: receiving NIC doesn’t send ACKs or NAKs to sending NIC
  data in dropped frames recovered only if initial sender uses higher layer rdt (reliable data transfer, e.g., TCP), otherwise dropped data lost
Ethernet’s MAC protocol: unslotted CSMA/CD with binary backoff

## Slide 70: 802.3 Ethernet standards: link & physical layers
  different physical layer media: fiber, cable
application
transport
network
link
physical
MAC protocol
and frame format
100BASE-TX
100BASE-T4
100BASE-FX
100BASE-T2
100BASE-SX
100BASE-BX
fiber physical layer
copper (twister pair) physical layer
many different Ethernet standards
  common MAC protocol and frame format
  different speeds: 2 Mbps, 10 Mbps, 100 Mbps, 1Gbps, 10 Gbps, 40 Gbps

## Slide 71: Link layer, LANs: roadmap
a day in the life of a web request
introduction
error detection, correction
multiple access protocols
LANs
  addressing, ARP
  Ethernet
  switches
  VLANs
link virtualization: MPLS
data center networking

## Slide 72: Ethernet switch
Switch is a link-layer device: takes an active role
  store, forward Ethernet frames
  examine incoming frame’s MAC address, selectively forward frame to one-or-more outgoing links when frame is to be forwarded on segment, uses CSMA/CD to access segment
transparent: hosts unaware of presence of switches
plug-and-play, self-learning
  switches do not need to be configured

## Slide 73: Switch: multiple simultaneous transmissions
switch with six interfaces (1,2,3,4,5,6)
A
A’
B
B’
C
C’
1
2
3
4
5
6
hosts have dedicated, direct connection to switch
switches buffer packets
Ethernet protocol used on each incoming link, so:
  no collisions; full duplex
  each link is its own collision domain
switching: A-to-A’ and B-to-B’ can transmit simultaneously, without collisions

## Slide 74: Switch: multiple simultaneous transmissions
switch with six interfaces (1,2,3,4,5,6)
A
A’
B
B’
C
C’
1
2
3
4
5
6
hosts have dedicated, direct connection to switch
switches buffer packets
Ethernet protocol used on each incoming link, so:
  no collisions; full duplex
  each link is its own collision domain
switching: A-to-A’ and B-to-B’ can transmit simultaneously, without collisions
  but A-to-A’ and C to A’ can not happen simultaneously

## Slide 75: Switch forwarding table
A
A’
B
B’
C
C’
1
2
3
4
5
6
Q: how does switch know A’ reachable via interface 4, B’ reachable via interface 5?
A: each switch has a switch table, each entry:
  (MAC address of host, interface to reach host, time stamp)
  looks like a routing table!
Q: how are entries created, maintained in switch table?
  something like a routing protocol?

## Slide 76: Switch: self-learning
A
A’
B
B’
C
C’
1
2
3
4
5
6
switch learns which hosts can be reached through which interfaces
A A’
Source: A
Dest: A’
MAC addr interface TTL
Switch table
(initially empty)
A
1
60 min
  when frame received, switch “learns” location of sender: incoming LAN segment
  records sender/location pair in switch table

## Slide 77: Switch: frame filtering/forwarding
when frame received at switch:
  1. record incoming link, MAC address of sending host
  2. index switch table using MAC destination address
  3. if entry found for destination then {
  if destination on segment from which frame arrived then drop frame
  else forward frame on interface indicated by entry
  }
  else flood /* forward on all interfaces except arriving interface */

## Slide 78: Self-learning, forwarding: example
A
A’
B
B’
C
C’
1
2
3
4
5
6
A A’
Source: A
Dest: A’
MAC addr interface TTL
switch table
(initially empty)
A
1
60
A A’
A A’
A A’
A A’
A A’
A’ A
A’
4
60
frame destination, A’, location unknown:
flood
destination A location known:
selectively send
on just one link

## Slide 79: Interconnecting switches
self-learning switches can be connected together:
Q: sending from A to G - how does S1 know to forward frame destined to G via S4 and S3?
A: self learning! (works exactly the same as in single-switch case!)
A
B
S1
C
D
E
F
S2
S4
S3
H
I
G

## Slide 80: Self-learning multi-switch example
Suppose C sends frame to I, I responds to C
Q: show switch tables and packet forwarding in S1, S2, S3, S4
A
B
S1
C
D
E
F
S2
S4
S3
H
I
G

## Slide 81: Small institutional network
to external
network
router
IP subnet
mail server
web server

## Slide 82: Switches vs. routers
application
transport
network
link
physical
network
link
physical
link
physical
switch
datagram
application
transport
network
link
physical
frame
frame
frame
datagram
6-82
both are store-and-forward:
routers: network-layer devices (examine network-layer headers)
switches: link-layer devices (examine link-layer headers)
both have forwarding tables:
routers: compute tables using routing algorithms, IP addresses
switches: learn forwarding table using flooding, learning, MAC addresses

## Slide 83: Link layer, LANs: roadmap
a day in the life of a web request
introduction
error detection, correction
multiple access protocols
LANs
  addressing, ARP
  Ethernet
  switches
  VLANs
link virtualization: MPLS
data center networking

## Slide 84: Virtual LANs (VLANs): motivation
Computer
Science
EE
Q: what happens as LAN sizes scale, users change point of attachment?
single broadcast domain:
  scaling: all layer-2 broadcast traffic (ARP, DHCP, unknown MAC) must cross entire LAN
  efficiency, security, privacy issues

## Slide 85: Virtual LANs (VLANs): motivation
administrative issues:
CS user moves office to EE - physically attached to EE switch, but wants to remain logically attached to CS switch
Computer
Science
EE
single broadcast domain:
  scaling: all layer-2 broadcast traffic (ARP, DHCP, unknown MAC) must cross entire LAN
  efficiency, security, privacy, efficiency issues
Q: what happens as LAN sizes scale, users change point of attachment?

## Slide 86: Port-based VLANs
1
8
2
7
9
16
10
15
switch(es) supporting VLAN capabilities can be configured to define multiple virtual LANs over single physical LAN infrastructure.
Virtual Local Area Network (VLAN)
port-based VLAN: switch ports grouped (by switch management software) so that single physical switch ……
…
EE (VLAN ports 1-8)
CS (VLAN ports 9-15)
…
… operates as multiple virtual switches
1
8
2
7
EE (VLAN ports 1-8)
…
9
16
10
15
…
CS (VLAN ports 9-15)

## Slide 87: Port-based VLANs
1
8
2
7
9
16
10
15
…
EE (VLAN ports 1-8)
CS (VLAN ports 9-15)
…
traffic isolation: frames to/from ports 1-8 can only reach ports 1-8
  can also define VLAN based on MAC addresses of endpoints, rather than switch port
dynamic membership: ports can be dynamically assigned among VLANs
forwarding between VLANS: done via routing (just as with separate switches)
  in practice vendors sell combined switches plus routers

## Slide 88: VLANS spanning multiple switches
1
8
2
7
9
16
10
15
…
EE (VLAN ports 1-8)
CS (VLAN ports 9-15)
…
5
8
2
7
…
16
1
6
3
4
Ports 2,3,5 belong to EE VLAN
Ports 4,6,7,8 belong to CS VLAN
trunk port: carries frames between VLANS defined over multiple physical switches
  frames forwarded within VLAN between switches can’t be vanilla 802.1 frames (must carry VLAN ID info)
  802.1q protocol adds/removed additional header fields for frames forwarded between trunk ports

## Slide 89: 802.1Q VLAN frame format
802.1 Ethernet frame
dest.
address
source
address
data (payload)
CRC
preamble
type
2-byte Tag Protocol Identifier
(value: 81-00)
Tag Control Information
(12 bit VLAN ID field, 3 bit priority field like IP TOS)
Recomputed
CRC
802.1Q frame
dest.
address
source
address
data (payload)
CRC
preamble
type